## Slide 1
Implementation of an
Obstacle-Avoiding Robot
Arduino • Ultrasonic Sensor • L298N Motor Driver
CSE2102 | Microprocessor and Microcontrollers Lab
Department of Computer Science and Engineering
Begum Rokeya University, Rangpur
2nd Year | 1st Semester | Session 2023–2024
12 October 2026
CSE2102 | Microprocessor and Microcontrollers Lab
01

## Slide 2
Submitted By / Submitted To
SUBMITTED BY
NAME ID REGISTRATION NO
Mithun Chandra Sarker 12305011 000018528
Md Abdullah Al Khalid Alif 12305016 000018533
Md Rakibul Islam 12305039 000018556
Year: 2nd Year • Semester: 1st Semester • Session: 2023–2024
Department of Computer Science and Engineering
Begum Rokeya University, Rangpur
SUBMITTED TO
Marija Sultana
Assistant Professor
Department of Computer Science and Engineering
Begum Rokeya University, Rangpur
CSE2102 | Microprocessor and Microcontrollers Lab
02

## Slide 3
Introduction & Motivation
Why autonomy matters in a compact educational platform
From manual control
to independent motion.
Remote-controlled robots depend on an operator and communication range. This project develops a low-cost 2WD robot that senses its surroundings, chooses a safe path, and moves without supervision.
LEARNING FOCUS
Microcontroller interfacing • timing • control logic
CSE2102 | Microprocessor and Microcontrollers Lab
03

## Slide 4
Problem Statement
A robot must sense, decide, and act—without supervision
01
SENSE
A single forward sensor has limited spatial awareness.
02
DECIDE
The environment must be scanned to compare multiple paths.
03
ACT SAFELY
Invalid echoes require a fail-safe response, not blind motion.
CSE2102 | Microprocessor and Microcontrollers Lab
04

## Slide 5
Objectives
Five concrete engineering outcomes
LOW-COST PLATFORM
Autonomous 2WD chassis
DISTANCE SENSING
HC-SR04 obstacle detection
LEFT / RIGHT SCAN
SG90 servo at 150° / 30°
PWM MOTOR DRIVE
L298N dual H-bridge
TURN MANEUVERS
90° turns and 180° recovery
CSE2102 | Microprocessor and Microcontrollers Lab
05

## Slide 6
Scope of the Work
Deliberately focused on robust indoor autonomy
INCLUDED
Hardware assembly
Wiring and firmware
Control algorithm
Fail-safe logic
Testing and documentation
OUT OF SCOPE
SLAM
Computer vision
Advanced path planning
Wireless control
FOCUS / Low-cost autonomous obstacle avoidance in an indoor environment—with maximum educational value.
CSE2102 | Microprocessor and Microcontrollers Lab
06

## Slide 7
System Architecture
Sensing → processing → power stage → actuation
HC-SR04 + SG90
SENSING
ARDUINO UNO
PROCESSING CORE
L298N
DUAL H-BRIDGE
2 × TT MOTORS
ACTUATION
18650 BATTERY + 5V REGULATION
CSE2102 | Microprocessor and Microcontrollers Lab
07

## Slide 8
Hardware Components
Bill of materials and functional role
COMPONENT QUANTITY PURPOSE
Arduino Uno 1 Main controller
L298N Motor Driver 1 Motor control
TT Gear Motor 2 Robot locomotion
HC-SR04 Ultrasonic Sensor 1 Obstacle detection
SG90 Servo Motor 1 Sensor scanning
2WD Chassis 1 Robot frame
18650 Battery 1 Power source
Jumper Wires & Breadboard Various Connections
7805 Voltage Regulator 1 Stable 5V supply
CSE2102 | Microprocessor and Microcontrollers Lab
08

## Slide 9
Pin Mapping & Wiring
Deterministic I/O allocation for sensing and motor control
SIGNAL ARDUINO PIN NOTES
WIRING NOTES
Remove ENA/ENB jumpers on L298N.
A common ground is mandatory across Arduino, driver, sensor, servo, and battery.
ENA 3 Motor A enable (PWM)
IN1 7 Motor A input 1
IN2 6 Motor A input 2
IN3 5 Motor B input 1
IN4 4 Motor B input 2
ENB 11 Motor B enable (PWM)
TRIG 9 Ultrasonic trigger
ECHO 8 Ultrasonic echo
SERVO 10 Servo control
CSE2102 | Microprocessor and Microcontrollers Lab
09

## Slide 10
Overall Working Principle
A continuous sense–decide–act loop
01 SENSE
Trigger pulse → echo duration
Valid: 2–200 cm | Timeout: 12,000 µs
02 DECIDE
Distance = (duration × 0.0343) / 2
Obstacle when distance ≤ 30 cm
03 ACT
Forward • left • right • turnaround
PWM commands drive both motors
CSE2102 | Microprocessor and Microcontrollers Lab
10

## Slide 11
Control Logic / State Machine
Cruise at PWM 130; scan only when the forward path is blocked
CRUISE
PWM 130
OBSTACLE ≤ 30 cm?
STOP & SETTLE
150 ms
SCAN LEFT
150°
SCAN RIGHT
30°
COMPARE
LEFT vs RIGHT
TURN LEFT
PWM 230
TURN AROUND
800 ms
TURN RIGHT
PWM 230
CSE2102 | Microprocessor and Microcontrollers Lab
11

## Slide 12
Decision Logic & Tuning Parameters
All behavior is governed by explicit, testable constants
PARAMETER VALUE DESCRIPTION
DECISION RULE
| Left − Right | ≤ 5 cm
→ execute 180° turnaround
NORMAL_SPEED 130 Cruising PWM
TURN_SPEED 230 Turn PWM
UTURN_SPEED 230 180° turn PWM
OBSTACLE_LIMIT 30 cm Obstacle threshold
EQUAL_LIMIT 5 cm Equal-side tolerance
SERVO_CENTER 90° Center angle
SERVO_LEFT / RIGHT 150° / 30° Scan angles
TURN_90_TIME 400 ms 90° duration
TURN_180_TIME 800 ms 180° duration
CSE2102 | Microprocessor and Microcontrollers Lab
12

## Slide 13
Implementation / Software
Arduino IDE • Servo library • two-source-file structure
obstacle_avoiding_robot.ino
obstacle.cpp
Firmware separates sensing, decision-making, and actuation into small testable functions.
CONTROL CYCLE
setup() initialize pins, servo, serial
loop() main control cycle
getDistance() trigger, time, validate
scanSides() acquire left / right distances
forward() apply cruise PWM
stopCar() zero motor outputs
turnLeft() / turnRight() / turnAround()
CSE2102 | Microprocessor and Microcontrollers Lab
13

## Slide 14
Results & Test Cases
All 10 test cases passed without false observations
10 / 10
TEST CASE DESCRIPTION EXPECTED BEHAVIOR RESULT
Clear path No obstacles Forward motion PASSED
Obstacle left ≤ 30 cm left Turn right PASSED
Obstacle right ≤ 30 cm right Turn left PASSED
Obstacle front Both sides blocked 180° turnaround PASSED
Boundary test Exactly 30 cm Correct turn PASSED
Invalid < 2 cm Sensor error Fail-safe stop PASSED
Echo timeout No echo Fail-safe stop PASSED
Invalid side Servo scan error Fail-safe action PASSED
CSE2102 | Microprocessor and Microcontrollers Lab
14

## Slide 15
System Output / Serial Monitor
9600 baud • live evidence for debugging and validation
> Front: 25 cm
> Front: INVALID
> Left: 40 cm
> Right: 35 cm
> Decision: Turn Left
VALID DISTANCE
Confirms echo timing and conversion.
INVALID READING
Triggers the fail-safe path.
SIDE SCAN + DECISION
Shows the evidence behind each maneuver.
CSE2102 | Microprocessor and Microcontrollers Lab
15

## Slide 16
A low-cost robot that can
sense, decide, and recover.
ACHIEVED
Validated 2WD autonomy with ultrasonic sensing, servo scanning, PWM motor control, and fail-safe behavior.
NEXT
Multi-sensor array • encoders / IMU • PID speed control • wireless monitoring • grid-based planning
Thank you. Questions?
CSE2102 | Microprocessor and Microcontrollers Lab
16